## Slide 1
ABOT
A Decentralized LoRa Mesh Communication Framework for Post-Disaster Environments
Aniraj Singh · Azzah Mallick
Department of CSE, Amity University, Uttar Pradesh, India
IEEE R10 HTC 2026
26 – 28 October 2026 | Bangkok, Thailand
Empowering Humanity Through Emerging Technology & Innovation
Notes: [Introduce yourself and your co-author, Azzah Mallick, Amity University.]
Title: ABOT, a decentralized LoRa mesh communication framework for post-disaster environments.

## Slide 2
Outline
From the problem to what we found
01
Why it matters
Motivation and existing work
02
The problem
Research gaps, our question, and ABOT's objectives
03
How we built it
Methodology and the four-layer design
04
What we found
Six results from simulation
05
What's next
Limitations and future work
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
02
Notes: [Optional, one line] I'll cover why this matters, the problem we set out to answer, how we built ABOT, what we found, and what comes next.

## Slide 3
Disasters are rising, and so are the losses
Introduction and motivation
Bangkok · severe flooding
Kashmir · forest fires in winter
5×
more reported weather- and climate-related disasters
1970 → 2019
≈3×
fewer deaths, thanks to better forecasts and early warnings
1970s → 2010s
7×
higher reported economic losses
1970s → 2010s
The hazard is only part of the problem: what matters just as much is how well our systems withstand it.
Source: WMO, Atlas of Mortality and Economic Losses from Weather, Climate and Water Extremes (1970–2019), 2021
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
03
Notes: I'd like to begin with something that connects the place we're meeting today with where I'm coming from.
Just last month, Bangkok experienced severe flooding, even back in India, Kashmir saw 48 forest fires in winters, a season when forests are normally damp.
These are different situations, but they bring us to a common concern: the challenges that environmental extremes pose to the systems we depend on. And the scale of these challenges is significant.
[CLICK 1] According to the World Meteorological Organization, the number of reported weather- and climate-, related disasters increased fivefold between 1970 and 2019. [CLICK 2] Yet, over the same period, the number of deaths decreased almost threefold because of better forecasting and early warnings. We have developed increasingly sophisticated ways to predict hazards, monitor environmental conditions, issue early warnings, and prepare for disasters.
We have become better at anticipating hazards and preparing people for them.
[CLICK 3] What goes unmentioned is that the reported economic losses from these disasters increased sevenfold between the 1970s and the 2010s. And when we talk about disasters, we often focus on the natural hazard itself. But the scale of the damage also depends on what happens to the infrastructure around us. Floods and earthquakes can damage roads, power lines, and communication towers. Poor planning, inadequate maintenance, and human negligence can make infrastructure even more vulnerable to failure.
So, while prevention, prediction, and resilient infrastructure are essential, we cannot assume that every disaster can be avoided or that every system will survive one. [CLICK 4] In other words, the hazard is only part of the problem. What matters just as much is how well our systems withstand it.

## Slide 4
What happens when the disaster strikes anyway?
Towers damaged: cellular and internet go down
Survivors can't call for help
Rescue teams struggle to coordinate
Keeping communication possible after infrastructure fails
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
04
Notes: That brings us to a question: what happens when the disaster strikes anyway?
[CLICK 1] When communication towers are damaged, cellular networks become unavailable, or internet connectivity is lost, survivors may be unable to call for help, and rescue teams may struggle to coordinate.
[CLICK 2] Preparing for disasters is one part of the challenge. Keeping communication possible after infrastructure has failed is another.
That is the problem that motivated our research.
Researchers have already explored several ways to address parts of this challenge. So, to understand where our work fits in, let's first look at the existing approaches to post-disaster communication.

## Slide 5
Existing work
Post-disaster communication: what is already out there
LoRa (Long Range radio)
LoRa (Long Range radio)
LPWAN disaster systems
LPWAN disaster systems
Titan [4]
Titan [4]
Consumer-grade LoRa platforms
Consumer-grade LoRa platforms
Meshtastic [12]
Meshtastic [12]
Disaster Radio
Disaster Radio
Project OWL · DuckLink [13]
Project OWL · DuckLink [13]
Routing research
Routing research
AI-optimised routing [7]
AI-optimised routing [7]
Power-aware routing [8]
Power-aware routing [8]
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
05
Notes: One technology that has received attention in this area is LoRa, or Long Range radio communication. It enables devices to exchange small amounts of data over long distances with relatively low power consumption, making it useful in situations where conventional connectivity may not be available.
Several existing systems have implemented this.
[CLICK 1] For example, Titan disaster management system which is based on low-power wide-area networks (LPWANs) LoRa. It’s an emergency command center app that helps people report danger instantly, tracks who is safe, and keeps phones connected even when the regular network crashes.
[CLICK 2] There are also Consumer-Grade LoRa Platforms like Meshtastic, Disaster Radio, and Project OWL that explore communication without relying on a conventional cellular network.
[CLICK 3] In particular, Project OWL uses portable DuckLink devices to establish communication networks in disaster-affected areas.
DuckLinks are custom hardware nodes (often packaged inside rugged little boxes). You can throw these "Ducks" out into an area hit by a hurricane, flood, or earthquake. Because they use LoRa, they automatically find each other and link up into a self-healing chain (called a ClusterDuck Network). If a regular person's cell phone loses service, they can still connect via Wi-Fi or Bluetooth to a nearby DuckLink. The message hops from Duck to Duck until it reaches a main gateway node.
[CLICK 4] Alongside these communication systems, researchers have also explored AI-based routing and power-aware routing. AI-optimized routing can improve packet delivery ratio (PDR) reduce end-to-end delay, and cut energy consumption in disaster-response mesh networks. AI (Artificial Intelligence) was tested to figure out the absolute best routes for data to travel from phone to phone. Messages got lost less often, showed up faster, and phones saved battery life. [CLICK 5] Further study on this also added that routing needs to be "power-aware", meaning it checks how much battery the next device in line has before sending data through it.
Together, these approaches provide an important foundation for our work.

## Slide 6
So why ABOT? Three recurring gaps
Existing work laid the foundation; the gaps show up when conditions change
1
Routing decisions
Link-quality routing exists, but uses static information or re-routes only after a failure
2
Simulation
LoRa simulators target protocol analysis, not fast, RL-ready training
3
Evaluation
Adaptive routing is rarely benchmarked across worsening damage levels
Decentralised mesh protocols that route by link quality
B.A.T.M.A.N.
Babel
OLSR
Compared on hardware: packet loss, delay, CPU and memory under load (Diniz et al., ICUAS 2025)
ABOT adds
LoRa radio limits
Five damage levels
An RL training interface
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
06
Notes: So, if these technologies already exist, why did we propose ABOT?
It isn't because the existing approaches have failed. They have established important foundations for post-disaster communication. However, the need to consider how that network behaves when conditions begin to change is. That is where three recurring gaps stood out.
[CLICK 1] The first was concerning routing decisions. Link-quality-aware routing exists, but approaches that rely on static information or recompute routes only after a failure may not respond continuously to deteriorating link conditions. [CLICK 2] The second was simulation. Existing LoRa simulators primarily focus on protocol analysis, rather than providing the fast, agent-compatible environment needed to train and evaluate reinforcement-learning-based routing.
[CLICK 3] And the third was evaluation. Adaptive routing is rarely benchmarked systematically across progressively worsening levels of infrastructure damage.
[CLICK 4] B.A.T.M.A.N, Babel and OLSR are existing decentralised systems that pick routes by link quality. They have real hardware validations for packet loss and delay, processor and memory use, varying traffic load and mobile nodes. [CLICK 5] ABOT extends its scope by using LoRa's radio limits, various damage levels and RL interface. ABOT is aimed towards disaster management.

## Slide 7
Problem statement
What we set out to answer
1
Central gateway dependency
single point of failure
2
Static routing decisions
limited adaptation to changing link quality
3
Reactive route recalculation
routes change only after a failure
4
Limited simulation scalability
hard to evaluate learning-based routing at scale
5
Limited damage-level evaluation
adaptive routing not tested across rising damage
RESEARCH QUESTION
How can routing in a gateway-free LoRa mesh use continuously updated link-state information, and how do classical and RL-based routing compare as network damage increases?
A comparison, studied entirely in simulation
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
07
Notes: This brings us to the central problem addressed in our paper.
When common communication systems fail, either entirely (complete infrastructure collapse) or partially (patchy failure), during large-scale disasters, a communication network must continue operating. LoRa radios suit this setting, but standard LoRa networks route through central gateways, which become a single point of failure. a gateway-free mesh is more practical, however, routing decisions need to account for changing network conditions, and the approaches used to make those decisions must be evaluated under realistic patterns of progressive degradation.
[CLICK 1] how can routing in a gateway-free LoRa mesh use continuously updated link-state information, and how do classical and reinforcement-learning-based routing approaches compare as network damage increases?

## Slide 8
ABOT: three objectives
A decentralized LoRa mesh framework for post-disaster environments
Decentralized mesh
Every node is both a terminal and a relay; no central gateway
Live link-state routing
Routes use continuously updated link quality
Fast simulation backend
A vectorized simulator to compare routing across five damage-severity presets
Investigated entirely in simulation · The RL part is exploratory
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
08
Notes: This is where ABOT comes in. We investigate these questions entirely in simulation.
We develop ABOT around three objectives: a decentralized mesh in which each node acts as both a terminal and a relay, routing that uses live link-state information, and a vectorized simulation backend for evaluating routing approaches across five damage-severity presets.

## Slide 9
How ABOT works
Every node is both a terminal and a relay
+
Survivor
Rescue node
SOS
1
Beacons
Nodes announce themselves to find neighbours and measure link quality
2
SOS + GPS
Hops node to node until it reaches an active rescue node
3
Live link state
PDR · RSSI · reachability: routes are re-assessed as nodes fail or links degrade
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
09
Notes: To investigate these questions, we propose ABOT — a decentralized LoRa-based mesh communication framework designed for post-disaster environments where conventional communication infrastructure may be unavailable or severely disrupted.
So, what does that actually mean?
Think about how our phones normally communicate. We generally depend on cellular towers or other existing network infrastructure to get our messages where they need to go.
ABOT takes a different approach. Instead of depending on a central gateway, every node in the network can act as both a terminal, which sends and receives messages, and a relay, which forwards messages for other nodes.
In other words, a device doesn't just communicate for itself. It can also help other devices communicate.
How does this work?
[CLICK 1] When a node joins the network, it broadcasts short signals called beacons to discover neighboring nodes. These beacons help nodes identify nearby connections and monitor the quality of the links between them. Together, the nodes form a decentralized mesh.
[CLICK 2] Now, imagine a survivor sending an SOS message containing their GPS coordinates.
The message can travel from one node to another, hop by hop, through the mesh until it reaches an active rescue node. From there, it can be relayed onward to emergency responders.
[CLICK 3] ABOT is designed to account for changing conditions where Nodes can fail, move out of range, or experience deteriorating connections.. Each node monitors information such as packet delivery ratio, signal strength, and neighbor reachability. Routing can then use this changing link-state information to reassess which paths are preferable, rather than relying only on a route established earlier.

## Slide 10
Methodology: a simulated disaster testbed
A virtual LoRa mesh with no central tower
Safe zone
Safe zone
10 × 10 grid · 100 nodes · 400 m apart
Dashed circle: the 1.5 km radio range of one node
Scale-up runs: 15 × 15 and up to 30 × 30 (900 nodes)
Two safe zones at the corners: the goal for every message
Five damage-severity presets (default: heavy)
intact
moderate
heavy
severe
extreme
Radio collisions: a sufficiently stronger signal wins (6 dB capture)
Node failures: sudden, or gradual as batteries drain
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
10
Notes: We have built a virtual disaster environment in which each radio represents a LoRa node in a decentralized mesh network, without a central tower.
Our primary setup uses a 10-by-10 grid, with nodes spaced 400 metres apart. We also used 15-by-15 and 30-by-30 grids for speed testing. The environment has two radios positioned at opposite corners of the grid which represent the safe zones that messages need to reach.
[CLICK 1] The network was tested under five damage-severity presets: intact, moderate, heavy, severe, and extreme, with heavy as the default. [CLICK 2] The simulation accounts for radio collisions, where a sufficiently stronger signal or louder signal gets priority. [CLICK 3] Radio failure scenarios include sudden failure or gradual deterioration as their batteries drain.

## Slide 11
Methodology: from protocol to benchmark
How every experiment is put together
1 Protocol
Beacon every 30 s
Link score: PDR over the last 50 packets
Gossip3: forward 75%, stay quiet after 3 copies
2 Routing task
Random start → a safe zone
1 hop = 10 s of simulated time
Seeded, reproducible trials
3 Simulators
SimPy reference: one event at a time
Time-stepped: all radios together, built for AI training
4 PPO router
Picks the next neighbour
3 training runs × 200,000 steps
Default settings
5 Benchmark
Classical planners: Dijkstra and A*
Static and dynamic versions
Same setup, five damage levels
Every routing approach runs in the same framework, across the same damage levels
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
11
Notes: Next, we implemented the communication protocol.
The protocol says that each node announces its presence through a beacon every 30 seconds. Nodes also maintain a live link-quality score based on packet delivery ratio, or PDR — in simple terms, the proportion of packets successfully received over the last 50 packets.
For message forwarding, we use a Gossip3 approach. Each radio forwards an SOS message with a 75 percent probability and suppresses its own forwarding when it has already heard three duplicate copies. This helps reduce unnecessary transmissions.
[CLICK 1] We then defined the routing task. A message starts at a randomly selected radio and must reach a safe zone. Each simulated hop advances time by 10 seconds, and one trial, or episode, represents a complete routing attempt. We use random seeds to control the random setup, allowing experiments to be reproduced and compared under controlled conditions.
[CLICK 2] To support reinforcement-learning experiments, we developed two versions of the simulator: the original SimPy-based backend and a faster, time-stepped backend designed to accelerate AI training.
[CLICK 3] For the learning-based router, we used Proximal Policy Optimization, or PPO. The agent selects a neighboring node as its next routing action. We trained it three separate times, using 200,000 environment steps for each training run and the default training settings.
[CLICK 4] Finally, we benchmarked the routing approaches against classical route planners. This allowed us to compare their behavior under the same general experimental framework and across different levels of simulated damage.

## Slide 12
System design: four layers
Paper Fig. 1 · The architecture of every ABOT node, inside a simulation harness
↓ Decisions go down
Layer 4 picks the next hop; Layer 2 sends it as a LoRa transmission
↑ Measurements go up
Received frames → de-duplicated beacons → PDR, RSSI and reachability for routing
Dashed box: the harness
Used only to train and evaluate; not part of a deployed node
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
12
Notes: The system design for ABOT was based on four layers, each responsible for a different part of communication.
[Added for this slide: walking through paper Fig. 1]
This is the architecture figure from our paper. Read it from the bottom up. Layer 1 is the LoRa radio itself. Layer 2 decides when a node transmits and how messages are passed on. Layer 3 turns what each node hears into link-quality measurements. Layer 4 uses those measurements to choose the route.
[CLICK 1] Decisions flow down the left side: the routing layer selects the next hop, and that becomes a radio transmission.
[CLICK 2] Measurements flow up the right side: received frames become de-duplicated beacon arrivals, and those become link metrics (packet delivery ratio, signal strength and reachability) that the routing layer reads. Between Layers 3 and 4, the learning agent receives its view as a list of 24 numbers.
[CLICK 3] The dashed box around everything is the simulation harness. We use it only to train and evaluate the routing methods; it isn't part of the software a real node would run.
Next, I'll go through the layers one at a time.
[If asked]
- "The figure says PPO may replace the solver. Does it?" The figure shows the option. In our results PPO is exploratory: it lands in the same range as the classical planners but doesn't beat the fastest ones.
- "How does each node know the whole network to run Dijkstra?" In the simulation the planners get a full view of the network, as a best case. Sharing link state across the mesh, and the airtime that costs, is future work.

## Slide 13
System design: layer by layer
Each layer handles one part of communication
L4
Routing & evacuation
L4
Routing & evacuation
L3
Link-state monitoring
L3
Link-state monitoring
L2
MAC & forwarding
L2
MAC & forwarding
L1
Physical (LoRa)
L1
Physical (LoRa)
Battery & failure model
Battery & failure model
Layer 1 · Physical (LoRa)
865 MHz band · +20 dBm
Spreading factor 12 · 125 kHz: ≈2.5 s of airtime per frame
Payload of at most 51 bytes
Log-distance path loss plus shadowing (rubble, walls)
Five severity presets, intact → extreme
Layer 2 · MAC & forwarding
Slotted ALOHA: a stronger signal survives a collision if it is 6 dB ahead
Gossip3: forward with 75% probability; stay quiet after 3 duplicates
Geo-greedy: hand the message to a neighbour closer to its destination
34-byte header · TTL 16 hops · cache of the last 256 message IDs
Layer 3 · Link-state monitoring
A beacon from every node every 30 s
PDR over the last 50 packets
RSSI: received signal strength
Reachability: neighbours heard recently
Each node builds its own view; no central monitor
Layer 4 · Routing & evacuation
Dynamic Dijkstra: shortest path on live link state; re-plans when the route ahead degrades
PPO agent (exploratory): learns to pick the next neighbour
Compares classical and learning-based routing
Battery & failure model
Linear battery drain over 300 s
Below 20% charge, outgoing links weaken in proportion
One failure per node per hour
Sudden · graceful · mixed (default) · burst
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
13
Notes: Layer 1: Physical Communication — LoRa
The first layer is the physical communication layer, which defines how nodes transmit radio signals.
We use the 865 MHz band, with a transmission power of plus 20 dBm, a spreading factor of 12, and a bandwidth of 125 kilohertz. This is the slowest, longest-range LoRa setting in our configuration, and each transmission has an airtime of approximately 2.5 seconds.
The maximum application payload is 51 bytes, so the protocol has to work within a very small message budget.
We also model how signals weaken over distance using a log-distance path-loss formula. A random shadowing term accounts for variations caused by obstacles such as rubble and walls.
To represent different levels of environmental damage, we use five severity presets: intact, moderate, heavy, severe, and extreme. These presets change the path-loss exponent and shadowing parameters, allowing us to simulate progressively harsher communication conditions.
[CLICK 1] Layer 2: MAC and Forwarding
The second layer manages channel access and message forwarding.
For channel access, we use slotted ALOHA with a capture mechanism. Nodes transmit in time slots, and when transmissions collide, the stronger signal can survive if it exceeds the next-strongest signal by the required capture threshold of 6 dB. Otherwise, both colliding transmissions are lost.
For forwarding, we use a combination of Gossip3 and geo-greedy unicast. With Gossip3, a node forwards a message with a 75 percent probability. If it hears three duplicate copies before its forwarding timer fires, it suppresses its own transmission. This reduces unnecessary transmissions.
Geo-greedy forwarding provides another option: a message can be sent directly to a neighboring node that is closer to its destination.
We also have a packet structure designed for constrained communication. Each packet has a 34-byte header containing information such as message identifiers, source and destination, priority, hop count, and time-to-live.
The time-to-live, or TTL, is set to 16 hops and decreases at every relay. Each node also maintains a cache of the last 256 message identifiers to identify and discard duplicate messages.
[CLICK 2] Layer 3: Link-State Monitoring
The third layer continuously monitors local network conditions.
Every node broadcasts a beacon every 30 seconds. Using the beacons it receives, each node tracks three metrics: packet delivery ratio, received signal strength indicator, or RSSI, and neighbor reachability.
PDR is calculated using a sliding window of the last 50 packets, giving each node an estimate of how reliably it can communicate. RSSI indicates the strength of the received signal, while reachability indicates how many known neighbors have been heard recently.
The important point is that this monitoring is decentralized. Every node derives its own local view of network conditions, without relying on a central monitoring system.
[CLICK 3] Layer 4: Routing and Evacuation
Finally, the fourth layer determines how messages should travel through the network toward a safe zone.
We evaluate two types of routing approaches: dynamic Dijkstra, a classical shortest-path algorithm that uses live network-state information, and an exploratory reinforcement-learning agent trained using PPO.
The dynamic Dijkstra planner can recalculate routes as link quality changes or nodes become unavailable. The PPO agent, meanwhile, learns to select a neighboring node based on its observations of the local network.
Comparing these approaches allows us to investigate how classical and learning-based routing behave under changing network conditions.
[CLICK 4] Battery and Failure Model
Alongside these four layers, we model battery depletion and node failures because both can affect network reliability.
The battery model applies linear drain over 300 seconds. Once a node's charge falls below 20 percent, its outgoing per-link delivery probability decreases proportionally with its remaining charge.
We use a failure rate of one failure per node per hour, and consider four failure modes.
The first is sudden failure, where a node stops operating immediately. The second is graceful failure, where its battery drains over time. The third is mixed failure, combining sudden and graceful failures in equal proportions; this is our default failure mode. The fourth is burst failure, where nodes within one grid cell of a disaster epicenter can fail together, excluding gateways.
Together, these design choices allow us to model not just message routing, but also the radio constraints, changing link conditions, battery limitations, and node failures that influence communication in a simulated post-disaster environment.

## Slide 14
Six results
What the simulations showed
1
Live link state helps
≈1.8× higher link-quality score
2
PPO ≈ classical planners
Same range, not better than the fastest
3
Damage sweep
Damage weakens long links, not trips
4
A faster simulator
Up to 7.3× faster than our reference
5
Gossip
No measurable difference yet
6
Radio model
Internally consistent with the standard model
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
14
Notes: The tested simulation gave results around six areas (or gave six results).

## Slide 15
Live link state: ≈1.8× higher link-quality score
Result 1 of 6 · Dijkstra with and without live link scores · the same 100 trips, 10×10 grid
Average link-quality score along the route
0
0.1
0.2
0.3
Static
hop count
0.145
Dynamic
live link score
0.267
≈1.8× higher
1.5–1.9× across all five damage levels
1.9–2.6×
comparing only trips of the same length: longer routes score lower, so the gap widens
1.03×
A* pair: re-planned in only 3 of 100 trips, so it tells us nothing either way
What is the link-quality score?
A 0–1 number each radio keeps for how well its links have worked recently, averaged over the radios on the route. A relative score for comparing route-finders, not the share of messages delivered.
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
15
Notes: For our routing approach the considered result was from running Dijkstra, the classic shortest-route method. The static version counted hops. The dynamic version also weighs each link by a live link-quality score, and re-plans if the route ahead gets worse. It was ran on the same 100 trips.
A link-quality score is a number from 0 to 1 that each radio keeps for how well its links have worked recently. We average it over the radios a route passes through. Read it as a relative score for comparing route-finders, not as the share of messages delivered.
[CLICK 1] Without live link scores, avg link quality score is 0.145, with link score its 0.267. it is about 1.8 times higher across damage levels. Dynamic versions take longer routes but they tend to score lower. [CLICK 2] If we compare only trips pdf the same length the gap widens to 1.9 to 2.6 times. (All of this is reference to link quality scores).
[CLICK 3] We also tested the A-star pair, a close cousin of Dijkstra, the same way. It re-planned in only 3 of 100 trips, so it shows almost no gap, 1.03 times, and tells us nothing either way.

## Slide 16
PPO lands in the same range as classical planners
Result 2 of 6 · Average hops to a safe zone · 100 trips per agent per grid
3 fastest classical planners
PPO (AI)
Dynamic Dijkstra
1
2
3
4
5
2.17
2.48
3.23
10 × 10 grid
3.23–3.25
3.56
4.40
15 × 15 grid
Success ≈100% for every agent, so we compare route length
PPO: trial-and-error learning, with points for good moves and penalties for bad ones
vs dynamic Dijkstra
PPO takes fewer hops on both grids
p = 2.5×10−5 and 1.9×10−3
vs the 3 fastest planners
10×10: slightly more hops (p = 0.047)
15×15: no significant difference (p = 0.255)
Learns a sensible route, but doesn't beat simple shortest-route methods → exploratory
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
16
Notes: second finding was that the ai route finder is in same range as the classical methods.
The ai finder was trained with ppo and a trial and error method that learns from point system. The point system said that there were points for good moves and penalties for bad ones.
The previous classical route finders – dij, a star each static and dynamic, were compared with this method on two grid sizes and same number of trips (aka 100).
[CLICK 1] The results show that AI takes fewer hops than dijisktra dynamic on 10x10 grid givning 2.48average hops with dijisktra having 3.23, as well as 15x15 grid with 3.56 and 4.40 for dijikstra.
[CLICK 2] The p values come well below the usual 0.05 bar being slightly worse at 10x10 compared against three fastest (0.047 just under the bar),and no significant difference at 15x15 (0.255).
[CLICK 3] It learned a sensible way to route, but on this task it doesn’t beat simple shortest-route methods. That’s why we call the AI part exploratory

## Slide 17
Damage weakens long links, but trips still succeed
Result 3 of 6 · Five damage levels (relative stress settings) · 250 trips per route-finder per level
Distance at which a single link works half the time
our mesh: 400 m – 1.5 km
0
0.5
1
1.5
2
2.5 km
intact
far beyond range
moderate
far beyond range
heavy
≈2 km
severe
≈1 km
extreme
≈640 m
Severe is the first level where links within range fail often
Heavy: halfway point ≈2 km, outside our range
Severe: ≈1 km, inside it
99.6%
of trips: PPO reaches a safe zone at every damage level
1 trip in 250 fails · classical planners: 100%
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
17
Notes: Third result was based on the damage preset. We made the damage worse, adjusting across the five levels. More damage makes radio signals fade faster with distance, as rubble would. Every route-finder ran 250 trips at each level, in five groups of 50.
[CLICK 1] At heavy, a link works half the time at about 2 kilometres, beyond our 1.5-kilometre radio range. At severe, that point moves inside the range, to about 1 kilometre. [CLICK 2] So severe is the first level where links within range fail often.
[CLICK 3] The AI doesn’t get worse as damage grows. It reaches a safe zone in 99.6 percent of trips at every level, which is one trip in 250.

## Slide 18
The AI's one weak spot: a livelock
Result 3 of 6 (continued) · Reward per trip: a normal trip scores just over 100
4 of 5 seed groups
101.4 – 102.2
average reward, at every damage level
The 4th seed group
≈17 · ≈23
intact to heavy · severe and extreme
The stuck loop
Picks neighbour slot 0 again
It has died: rejected, −20
Next view looks almost the same
Cause: a fixed list of 8 neighbours, where dead ones stay listed
Same group at every level, even intact: a design issue, not damage
Damage weakens long links but doesn't stop trips: the sweep compares route-finders under rising stress
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
18
Notes: Each trip also earns a points score, called reward, and a normal trip scores just over 100. Four of the AI’s five groups average 101.4 to 102.2. [CLICK 1] The fourth averages only about 17 from intact to heavy, and about 23 at severe and extreme.
[CLICK 2] The AI’s one weak spot is a livelock, a stuck loop. In one test scenario, it keeps picking a neighbour that has died. Each try is rejected with a penalty, the situation looks almost the same, so it picks that neighbour again. The cause is its fixed list of eight neighbours, where dead ones stay listed. [CLICK 3] It happens at every damage level, including intact. So the weak spot is how the AI’s choices are set up, not the damage.
[CLICK 4] So in our setup, damage weakens the long links, but it doesn’t stop trips. Success stays near 100 percent. This sweep compares route-finders under rising stress.

## Slide 19
A faster simulator for RL training
Result 4 of 6 · Time-stepped backend vs our own SimPy reference, collisions on
Reference (SimPy): one transmission event at a time
Time-stepped: every radio moves forward together
Each event handled separately: accurate, but slow for AI training
One shared time step for all radios, same models for links, failures and collisions
up to
7.3×
faster than our reference simulator
≈4.7× at the 10×10 grid used for the main results
Training needs 200,000 practice steps per run
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
19
Notes: Fourth, Our first simulator handles each radio transmission as a separate event. That's accurate, but too slow for AI training, which needed 200,000 practice steps per run. [CLICK 1] So we built a faster one that moves all the radios forward together, one time step at a time, using the same models for radio links, failures and collisions. [CLICK 2] The newer simuklator runs upto 7.3 times faster than our own reference simulator. A collision is when two radios send at once and garble each other.

## Slide 20
Gossip: no measurable difference
Result 5 of 6 · AI with gossip on vs off · 3 training runs × 300 trips per setting
Gossip: radios pass information to neighbours, who pass it on, like a rumour.
Here: the AI's value estimate for each position.
Metric
Gossip on
Gossip off
p-value
Reached a safe zone
100%
100%
–
Average hops
2.487
2.497
0.842
Average reward
101.42
101.27
0.826
Both p-values are far above 0.05: no measurable difference
Why: the merge step, where a radio combines received values with its own, isn't connected yet, and both settings already solve the task.
→ The system works without gossip; this doesn't show gossip helps.
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
20
Notes: Fifth, was gossip. Gossip means radios passing information to their neighbours, who pass it on, like a rumour. Here, radios share the AI’s estimates of how good each position is. We ran the AI with gossip on and off, with three training runs and 300 trips for each setting.
[CLICK 1] Both settings reached a safe zone in every trip. Average hops were 2.487 with gossip and 2.497 without, with a p-value of 0.842. Average reward was 101.42 against 101.27, with a p-value of 0.826. Both are far above 0.05.
[CLICK 2] So gossip made no difference. Its merge step, where a radio would combine the values it receives with its own, isn’t connected yet, and both settings already solve this task. This shows the system works without gossip, not that gossip helps.

## Slide 21
The radio model is internally consistent
Result 6 of 6 · Link delivery (PDR) vs distance from the channel model (paper Fig. 2)
≈640 m
≈1 km
≈2 km
Log scale: each labelled gridline is 10× further. Shaded band: our mesh, 400 m to 1.5 km.
A link works half the time at
heavy ≈2 km
severe ≈1 km
extreme ≈640 m
At 1.5 km: 66% · 29% · 11%
heavy · severe · extreme
At 400 m: above 73% at every level
Internal consistency, not agreement with real radios
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
21
Notes: Lastly, the radio model that we used. how often a single link gets a message through as distance grows. That’s called the packet delivery ratio, or PDR.
The distance axis is a log scale, so each labelled gridline is ten times further. The band between the dashed lines, from 400 metres to 1.5 kilometres, is where our mesh operates.
[CLICK 1] Each curve is one damage level, a relative stress setting, and more damage shifts the curve left. At heavy, a link works half the time at about 2 kilometres. At severe, about 1 kilometre. At extreme, about 640 metres. [CLICK 2] At 1.5 kilometres, links succeed 66 percent of the time at heavy, 29 percent at severe and 11 percent at extreme. [CLICK 3] At 400 metres, the nearest neighbours, they stay above 73 percent at every level.
[CLICK 4] The radio model behaves the way the standard model predicts: more distance and more damage mean more failures. That shows internal consistency, not agreement with real radios. It also explains the damage result: severe is where the halfway point moves inside our radio range.

## Slide 22
Limitations
What the results do, and don't, show
1
Simulation only
No hardware validation yet: read every result as a simulation finding
2
Radio airtime
30 s beacons at SF12 ≈ 4.4% channel occupancy per node; a compliant schedule could shift beacon-dependent results
3
RL is exploratory
The 8-neighbour action space causes the livelock; value estimates were inconsistent across the 3 training runs
4
Score ≠ delivery
The link-quality score is not end-to-end SOS delivery; measuring that is the next step
5
Adoption
Needs enough devices and relays; participation can't be assumed
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
22
Notes: There are certain drawbacks to abot.
[CLICK 1] First, ABOT has been evaluated entirely in simulation. We have not yet validated its performance on physical hardware, so the results should be understood as simulation-based findings rather than evidence of real-world deployment.
[CLICK 2] There are also practical radio constraints to address. Our current 30-second beacon interval results in approximately 4.4 percent channel occupancy at SF12, which exceeds the 1 percent duty-cycle limit specified by ETSI for the relevant band. A compliant transmission schedule would therefore need to be investigated, and it could affect the results that depend on the beacon rate.
[CLICK 3] Second, there are limitations in the routing and learning components. The reinforcement-learning agent has a constrained action space of eight neighbors, even though the network can have substantially more neighbors.
This restriction contributes to a live lock problem in which the agent can repeatedly select an invalid neighbor.
We also observed inconsistent value-estimation performance across the three training seeds, indicating that the reinforcement-learning component requires further investigation. At this stage, the learning-based routing approach remains exploratory; our results do not establish that it consistently outperforms classical routing methods.
[CLICK 4] Another important distinction is that PDR is used as a link-quality measure in our routing experiments. It should not be interpreted as a direct measurement of successful end-to-end SOS delivery. Measuring that outcome explicitly is an important next step.
[CLICK 5] Finally, real-world adoption presents its own challenge. A decentralized communication system depends on enough devices and relays being available to establish useful connectivity. That participation cannot simply be assumed. These limitations define what still needs to be addressed before ABOT can be considered for practical deployment.

## Slide 23
Future work
From a simulation framework toward real-world validation
1
STEP 1
Measure
End-to-end SOS delivery, plus adaptive beaconing to cut airtime
2
STEP 2
Validate
On physical LoRa hardware: timing, interference, real radio behaviour
3
STEP 3
Integrate
With existing LoRa platforms and search-and-rescue systems
4
STEP 4
Improve RL
Fix the action space, stabilise training, test larger networks and harsher failures
5
STEP 5
Adopt
Responders → pre-positioned relays → the public, with disaster-management authorities
Goal: from simulation to a system validated under real disaster-response conditions
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
23
Notes: Moving forward, we have identified several directions for further development.
[CLICK 1] First, we want to measure end-to-end SOS packet delivery directly, rather than relying primarily on link-level PDR. We also need to investigate adaptive beaconing, which could help reduce channel occupancy while allowing nodes to remain aware of changing network conditions.
[CLICK 2] Second, the framework needs to be validated on physical LoRa hardware. This would allow us to compare simulation results with actual radio behavior and investigate the practical effects of transmission timing, interference, and other hardware-level constraints.
[CLICK 3] We also aim to explore integration with existing decentralized communication platforms and search-and-rescue systems. As discussed in our paper, ABOT is designed with compatibility with existing LoRa hardware in mind, and integration with search-and-rescue platforms is an important step toward practical use.
[CLICK 4] On the routing side, future work should address the constrained action space and improve the stability of the reinforcement-learning agent. Further experiments can establish whether learning-based routing offers benefits under larger networks and more demanding failure conditions.
[CLICK 5] Finally, there is the question of adoption. A practical rollout could begin with responder devices and pre-positioned relay nodes before expanding to broader public participation. Collaboration with disaster-management authorities and emergency-response organizations would be important in making such a system viable. Interdepartmental comm and real world imple.
[CLICK 6] Ultimately, our goal is to move from a simulation-based framework toward a system that can be validated, integrated, and evaluated under real-world disaster-response conditions.

## Slide 24
Thank You
Q&A
Aniraj Singh · Azzah Mallick
Department of CSE, Amity University, Uttar Pradesh, India
IEEE R10 HTC 2026 · Bangkok, Thailand
Empowering Humanity Through Emerging Technology & Innovation
IEEE R10 HTC 2026 | Bangkok, Thailand | 26 – 28 October 2026
24
Notes: [Thank the audience and invite questions.]